## Slide 1
Bell labs,
1947.
7Billion FET
2018
New Directions in Electronics
Notes: 1
To print: 1,4,5,7,8,9,15,16,18,23,24,25,26,29,30,31,34,35,40,41,43,46,47,48,51,55,60,61,62,63
Hosszutav jovo elektornikaja
Folztatni a miniaturiyalast  molekularis elektronika
Uj koncepciokat kidolgozni szamitasokra…
Kis meret tartomanyban maskeppen viselkedik egy eszkoz. Pl. Kvantummechanikailag,
Vagy ballisztikusan  elektron optika
Szamos objektum nanotechnologia teruleterol, amibol aramkoroket lehet kesziteni.

## Slide 2
Molecular
electronics
Spintronics
Lspin
Lφ
Le
LBohr
Quantumelectronics
Memristors
New Directions in Electronics
Notes: 2
To print: 1,4,5,7,8,9,15,16,18,23,24,25,26,29,30,31,34,35,40,41,43,46,47,48,51,55,60,61,62,63
Hosszutav jovo elektornikaja
Folztatni a miniaturiyalast  molekularis elektronika
Uj koncepciokat kidolgozni szamitasokra…
Kis meret tartomanyban maskeppen viselkedik egy eszkoz. Pl. Kvantummechanikailag,
Vagy ballisztikusan  elektron optika
Szamos objektum nanotechnologia teruleterol, amibol aramkoroket lehet kesziteni.

## Slide 3
Towards quantum
MosFET: Bottleneck is leakage
Atoms, molecule: Full quantum description
Schrödinger equation  Periodic table
Nanoscale objects:
Small is different. E.g.
- Single electron transistor (Quantum dots)
- If L ≈ λF or L φ various quantum effects….
Notes: - In present chip industry quantum mechanics place a major limitation of further miniaturization. Insulator barriers with a few atom layer width. Gate leakage due to tunneling effect
- Scale of atoms and molecules, full quantum limit. Schrodinger equation dictates the behaviors, periodic table etc.
Nanoscale objects lambda_F comparable to the size: e.g. two tunnel barriers forming a quantum dot.
As long as quantum effects are a limitation for electrical engineer, a great advantage and playground for physicists. Try to take as an advantage…. Quantum behavior is richer than classical one.  Define controllable quantum systems with manipulation and read out possibility.

## Slide 4
Quantum in electronics
Nanoscale objects:
If L ≈ λF or L φ various quantum effects….
E.g. Quantum Dot (Artificial atom)
λF
λF
~
MosFET: Bottleneck is leakage
Notes: - In present chip industry quantum mechanics place a major limitation of further miniaturization. Insulator barriers with a few atom layer width. Gate leakage due to tunneling effect
- Scale of atoms and molecules, full quantum limit. Schrodinger equation dictates the behaviors, periodic table etc.
Nanoscale objects lambda_F comparable to the size: e.g. two tunnel barriers forming a quantum dot.
As long as quantum effects are a limitation for electrical engineer, a great advantage and playground for physicists. Try to take as an advantage…. Quantum behavior is richer than classical one.  Define controllable quantum systems with manipulation and read out possibility.

## Slide 5
Quantum in electronics
Nanoscale objects:
If L ≈ λF or L φ various quantum effects….
E.g. Quantum Dot (Artificial atom)
=
E
QD
E
λF
λF
~
Γ1
Γ2
=
See more: Fundamentals of Nanoelectronics, A. Palyi: Quantum Information Processing
MosFET: Bottleneck is leakage
Notes: - In present chip industry quantum mechanics place a major limitation of further miniaturization. Insulator barriers with a few atom layer width. Gate leakage due to tunneling effect
- Scale of atoms and molecules, full quantum limit. Schrodinger equation dictates the behaviors, periodic table etc.
Nanoscale objects lambda_F comparable to the size: e.g. two tunnel barriers forming a quantum dot.
As long as quantum effects are a limitation for electrical engineer, a great advantage and playground for physicists. Try to take as an advantage…. Quantum behavior is richer than classical one.  Define controllable quantum systems with manipulation and read out possibility.

## Slide 6
Quantum Dots
=
E
QD
E
λF
λF
~
Γ1
Γ2
=
discrete energy spectrum, εi
Coulomb interaction, UC
→ Coulomb blockade
Gate electrode to shift energy levels, Vg
Γ: coupling to electrodes
Gate assisted transport
Bias assisted transport
Notes: - In present chip industry quantum mechanics place a major limitation of further miniaturization. Insulator barriers with a few atom layer width. Gate leakage due to tunneling effect
- Scale of atoms and molecules, full quantum limit. Schrodinger equation dictates the behaviors, periodic table etc.
Nanoscale objects lambda_F comparable to the size: e.g. two tunnel barriers forming a quantum dot.
As long as quantum effects are a limitation for electrical engineer, a great advantage and playground for physicists. Try to take as an advantage…. Quantum behavior is richer than classical one.  Define controllable quantum systems with manipulation and read out possibility.

## Slide 7
Quantum Dots
=
E
QD
E
λF
λF
~
Γ1
Γ2
=
Gate assisted transport
Bias assisted transport
GII(2e2/h)
0
0.6
Gate voltage
Gate
Notes: - In present chip industry quantum mechanics place a major limitation of further miniaturization. Insulator barriers with a few atom layer width. Gate leakage due to tunneling effect
- Scale of atoms and molecules, full quantum limit. Schrodinger equation dictates the behaviors, periodic table etc.
Nanoscale objects lambda_F comparable to the size: e.g. two tunnel barriers forming a quantum dot.
As long as quantum effects are a limitation for electrical engineer, a great advantage and playground for physicists. Try to take as an advantage…. Quantum behavior is richer than classical one.  Define controllable quantum systems with manipulation and read out possibility.

## Slide 8
Quantum electronics
Quantum electronics:
Beside understand quantum effects the goal is to
create well defined quantum subsystems,
control and manipulate them
Take the advantage of QUANTUM!
Nanoscale objects:
If L ≈ λF or L φ various quantum effects….
MosFET: Bottleneck is leakage
Notes: - In present chip industry quantum mechanics place a major limitation of further miniaturization. Insulator barriers with a few atom layer width. Gate leakage due to tunneling effect
- Scale of atoms and molecules, full quantum limit. Schrodinger equation dictates the behaviors, periodic table etc.
Nanoscale objects lambda_F comparable to the size: e.g. two tunnel barriers forming a quantum dot.
As long as quantum effects are a limitation for electrical engineer, a great advantage and playground for physicists. Try to take as an advantage…. Quantum behavior is richer than classical one.  Define controllable quantum systems with manipulation and read out possibility.

## Slide 9
“When we get to the very, very small world… We can manufacture in different ways. We can use, not just circuits, but some system involving the quantized energy levels, or the interactions of quantized spins, etc.”
Feynman
Principles: Qubit
0
1
or
Classical
0
1
Quantum
Compared to a classical bit much more information can be encoded
Notes: Basic unit to store quantum information: qubit
Classical two level system, quantum two level system.
Kvantum mechanika alapjait erinto kerdeskor…
Fizika ket uj teruletenek a megszuletesehez vezetett…
Eroforrasava valt
Kvantum rendszerek szimulaciojat mar Feynman 82 megsejtette, 96 ban elso ilyen algoritmusok
Pl.:
Estimation of the eigenvalues and eigenvectors of a Hamiltonian (this algorithm invokes
the QFT), which can be used to find the energy levels of an atom for example [AL99].
• Simulation of the dynamics of many-body Fermi systems, using either first or second
quantized descriptions [AL97].
• Simulation of quantum chaos and localization [GS01].
Kvantum mechanika linearitasa miatt egy kvantum mechanikai logikai kapu
parhuzamosan transzformalja az osszes kombinaciojat a ket qubites allapotnak.
Jo tudni:
- Nehany fontos eset van, ahol exponencialisan jobb a kvantum szamitogep
- Normal szamitast pl. szamok osszeadasat nem gyorsitan fel a kvantum szamitogep
- Nem minden problema eseteben okoyna exponencialis sebesseg novekedest
Kvantum algoritmusok felfedezese uj dimenziokba helyezte fizika, szamitaselmelet es informacioelmelet tudomany agait.

## Slide 10
Principles: Qubit
Probability to get 0: |a|2
Probability to get 1: |b|2
Measurement QuBit 1 results in |1>
Nonlocality: manipulation of QuBit1 has consequence on QuBit2
Two qubit
+
Measurement
Entanglement
+
f quantum gate
Quantum parallelism: parallel evaluations grow exponentially with the number of Qubits (≈2n)
Qubit Hamiltionian
-pulse
0
0
-pulse
Control: RF techniques learned from NMR
Notes: Basic unit to store quantum information: qubit
Classical two level system, quantum two level system.
Kvantum mechanika alapjait erinto kerdeskor…
Fizika ket uj teruletenek a megszuletesehez vezetett…
Eroforrasava valt
Kvantum rendszerek szimulaciojat mar Feynman 82 megsejtette, 96 ban elso ilyen algoritmusok
Pl.:
Estimation of the eigenvalues and eigenvectors of a Hamiltonian (this algorithm invokes
the QFT), which can be used to find the energy levels of an atom for example [AL99].
• Simulation of the dynamics of many-body Fermi systems, using either first or second
quantized descriptions [AL97].
• Simulation of quantum chaos and localization [GS01].
Kvantum mechanika linearitasa miatt egy kvantum mechanikai logikai kapu
parhuzamosan transzformalja az osszes kombinaciojat a ket qubites allapotnak.
Jo tudni:
- Nehany fontos eset van, ahol exponencialisan jobb a kvantum szamitogep
- Normal szamitast pl. szamok osszeadasat nem gyorsitan fel a kvantum szamitogep
- Nem minden problema eseteben okoyna exponencialis sebesseg novekedest
Kvantum algoritmusok felfedezese uj dimenziokba helyezte fizika, szamitaselmelet es informacioelmelet tudomany agait.

## Slide 11
Nvidia GeForce GTX280
f is a quantum gate
Guild system
Mass production
Principles: How powerful?
Notes: Parallel computation gets common nowadays.
Resource, power in computation…
Kvantum mechanika alapjait erinto kerdeskor…
Fizika ket uj teruletenek a megszuletesehez vezetett…
Eroforrasava valt
Similar to changes, development in the Industrial Revolution
Previously, one master did the whole production from the beginning to the end, however there are products where it is much more efficient to devide the process into small simple tasks and do them parallel. This is a key ingredient of nowadays mass production.
A quantum computer operates with maximal parallel operation, since it operates on all possible states at the same time. In order to calculate so, NO NEED for special optimization, it is provided freely by quantum mechanics, it is how nature behaves. This property is the greatest potential, resource of quantum computing.
Quantum computer maximize the parallel operation. It simultaneously operates on all possible states. No need for several CPUs. It is provided freely by quamtum mechanics, by nature. This is the real resource, the great potential in quantum computing.
Resource, power in computation…
Kvantum mechanika alapjait erinto kerdeskor…
Fizika ket uj teruletenek a megszuletesehez vezetett…
Eroforrasava valt
Kvantum rendszerek szimulaciojat mar Feynman 82 megsejtette, 96 ban elso ilyen algoritmusok
Pl.:
Estimation of the eigenvalues and eigenvectors of a Hamiltonian (this algorithm invokes
the QFT), which can be used to find the energy levels of an atom for example [AL99].
• Simulation of the dynamics of many-body Fermi systems, using either first or second
quantized descriptions [AL97].
• Simulation of quantum chaos and localization [GS01].
Kvantum mechanika linearitasa miatt egy kvantum mechanikai logikai kapu
parhuzamosan transzformalja az osszes kombinaciojat a ket qubites allapotnak.
Jo tudni:
- Nehany fontos eset van, ahol exponencialisan jobb a kvantum szamitogep
- Normal szamitast pl. szamok osszeadasat nem gyorsitan fel a kvantum szamitogep
- Nem minden problema eseteben okoyna exponencialis sebesseg novekedest
Kvantum algoritmusok felfedezese uj dimenziokba helyezte fizika, szamitaselmelet es informacioelmelet tudomany agait.
Kvantum rendszerek szimulaciojat mar Feynman 82 megsejtette, 96 ban elso ilyen algoritmusok
Pl.:
Estimation of the eigenvalues and eigenvectors of a Hamiltonian (this algorithm invokes
the QFT), which can be used to find the energy levels of an atom for example [AL99].
• Simulation of the dynamics of many-body Fermi systems, using either first or second
quantized descriptions [AL97].
• Simulation of quantum chaos and localization [GS01].
Kvantum mechanika linearitasa miatt egy kvantum mechanikai logikai kapu
parhuzamosan transzformalja az osszes kombinaciojat a ket qubites allapotnak.
Jo tudni:
- Nehany fontos eset van, ahol exponencialisan jobb a kvantum szamitogep
- Normal szamitast pl. szamok osszeadasat nem gyorsitan fel a kvantum szamitogep
- Nem minden problema eseteben okoyna exponencialis sebesseg novekedest
Kvantum algoritmusok felfedezese uj dimenziokba helyezte fizika, szamitaselmelet es informacioelmelet tudomany agait.

## Slide 12
Quantum Bit
Multiple QuBits
Roadrunner - Los Alamos
Limit < 40 Qubit
Principles: How powerful?
Notes: Resource, power in computation…
Kvantum mechanika alapjait erinto kerdeskor…
Fizika ket uj teruletenek a megszuletesehez vezetett…
Eroforrasava valt
Kvantum rendszerek szimulaciojat mar Feynman 82 megsejtette, 96 ban elso ilyen algoritmusok
Pl.:
Estimation of the eigenvalues and eigenvectors of a Hamiltonian (this algorithm invokes
the QFT), which can be used to find the energy levels of an atom for example [AL99].
• Simulation of the dynamics of many-body Fermi systems, using either first or second
quantized descriptions [AL97].
• Simulation of quantum chaos and localization [GS01].
Kvantum mechanika linearitasa miatt egy kvantum mechanikai logikai kapu
parhuzamosan transzformalja az osszes kombinaciojat a ket qubites allapotnak.
Jo tudni:
- Nehany fontos eset van, ahol exponencialisan jobb a kvantum szamitogep
- Normal szamitast pl. szamok osszeadasat nem gyorsitan fel a kvantum szamitogep
- Nem minden problema eseteben okoyna exponencialis sebesseg novekedest
Kvantum algoritmusok felfedezese uj dimenziokba helyezte fizika, szamitaselmelet es informacioelmelet tudomany agait.

## Slide 13
Quantum Bit
Multiple QuBits
Quantum parallelism: parallel evaluations grow exponentially with the number of Qubits (≈2n)
Roadrunner - Los Alamos
Limit < 40 Qubit
+ 1 Qubit
Principles: How powerful?
Notes: Resource, power in computation…
Kvantum mechanika alapjait erinto kerdeskor…
Fizika ket uj teruletenek a megszuletesehez vezetett…
Eroforrasava valt
Kvantum rendszerek szimulaciojat mar Feynman 82 megsejtette, 96 ban elso ilyen algoritmusok
Pl.:
Estimation of the eigenvalues and eigenvectors of a Hamiltonian (this algorithm invokes
the QFT), which can be used to find the energy levels of an atom for example [AL99].
• Simulation of the dynamics of many-body Fermi systems, using either first or second
quantized descriptions [AL97].
• Simulation of quantum chaos and localization [GS01].
Kvantum mechanika linearitasa miatt egy kvantum mechanikai logikai kapu
parhuzamosan transzformalja az osszes kombinaciojat a ket qubites allapotnak.
Jo tudni:
- Nehany fontos eset van, ahol exponencialisan jobb a kvantum szamitogep
- Normal szamitast pl. szamok osszeadasat nem gyorsitan fel a kvantum szamitogep
- Nem minden problema eseteben okoyna exponencialis sebesseg novekedest
Kvantum algoritmusok felfedezese uj dimenziokba helyezte fizika, szamitaselmelet es informacioelmelet tudomany agait.

## Slide 14
Quantum Bit
Multiple QuBits
Quantum parallelism: parallel evaluations grow exponentially with the number of Qubits (≈2n)
Roadrunner - Los Alamos
Limit < 40 Qubit
+ 2 Qubit
Principles: How powerful?
Notes: Resource, power in computation…
Kvantum mechanika alapjait erinto kerdeskor…
Fizika ket uj teruletenek a megszuletesehez vezetett…
Eroforrasava valt
Kvantum rendszerek szimulaciojat mar Feynman 82 megsejtette, 96 ban elso ilyen algoritmusok
Pl.:
Estimation of the eigenvalues and eigenvectors of a Hamiltonian (this algorithm invokes
the QFT), which can be used to find the energy levels of an atom for example [AL99].
• Simulation of the dynamics of many-body Fermi systems, using either first or second
quantized descriptions [AL97].
• Simulation of quantum chaos and localization [GS01].
Kvantum mechanika linearitasa miatt egy kvantum mechanikai logikai kapu
parhuzamosan transzformalja az osszes kombinaciojat a ket qubites allapotnak.
Jo tudni:
- Nehany fontos eset van, ahol exponencialisan jobb a kvantum szamitogep
- Normal szamitast pl. szamok osszeadasat nem gyorsitan fel a kvantum szamitogep
- Nem minden problema eseteben okoyna exponencialis sebesseg novekedest
Kvantum algoritmusok felfedezese uj dimenziokba helyezte fizika, szamitaselmelet es informacioelmelet tudomany agait.

## Slide 15
Quantum algorithms
Quantum parallelism: all possibilities are analyzed at the same time – like searching through a database at once
Quantum gates: rotations on superpositions
Nature 543 (2017)
V. Cărare, APS
Notes: Coherence  Coupling to surrounding, for readout, manipulation
100 -1000 qubit system would be competitve
Quantum parallelism
the number of parallel function evaluations grows exponentially with the size of the
quantum computer
Kvantum mechanika alapjait erinto kerdeskor…
Fizika ket uj teruletenek a megszuletesehez vezetett…
Eroforrasava valt
Kvantum rendszerek szimulaciojat mar Feynman 82 megsejtette, 96 ban elso ilyen algoritmusok
Pl.:
Estimation of the eigenvalues and eigenvectors of a Hamiltonian (this algorithm invokes
the QFT), which can be used to find the energy levels of an atom for example [AL99].
• Simulation of the dynamics of many-body Fermi systems, using either first or second
quantized descriptions [AL97].
• Simulation of quantum chaos and localization [GS01].
Kvantum mechanika linearitasa miatt egy kvantum mechanikai logikai kapu
parhuzamosan transzformalja az osszes kombinaciojat a ket qubites allapotnak.
Jo tudni:
- Nehany fontos eset van, ahol exponencialisan jobb a kvantum szamitogep
- Normal szamitast pl. szamok osszeadasat nem gyorsitan fel a kvantum szamitogep
- Nem minden problema eseteben okoyna exponencialis sebesseg novekedest
Kvantum algoritmusok felfedezese uj dimenziokba helyezte fizika, szamitaselmelet es informacioelmelet tudomany agait.

## Slide 16
Blatt Quantum Machines, Les Houches Summer School (2011)
Technologies
Technology Roadmaps:
US http://qist.lanl.gov/,
EU http://qist ect it/Reports/
Quantum systems with
control and manipulation
possibility
Photons
Cavity QED
Trapped ions
Superconductors
NMR
Quantum dots
…
In situ Error corrections!!!
Notes: Photons, easy to detect, fast, but difficult to localize
Geszti course Domonkos Peter course

## Slide 17
Quantum towards Technology
One from the 3 Flagship project of the EU
2 x 5years program
Hungarian support program 3.2BHUF
http://qurope.eu/manifesto
Notes: Idea is to build S lead into a small quantum computer, which has two spin qubits. And by Single Quibit gates amnipulate spin state of the dot, then let a second electron to be injected from the superconductor and do state tomography.

## Slide 18
Quantum towards Technology
Notes: Idea is to build S lead into a small quantum computer, which has two spin qubits. And by Single Quibit gates amnipulate spin state of the dot, then let a second electron to be injected from the superconductor and do state tomography.

## Slide 19
- Qubit:
½ spin of single electron trapped into
a confinement potential
Spin Qubits
R. Hanson, Rev Mod Phys, 79, 1217 (2007)
Notes: A. Palyi course
The internal degree of freedom, spin. The rotation of electron. It is an idal two level system.
Advantages of spin qubits compare to other systems:
- Inherent scalability
Compatibility with existing microelectronics industry
well- defined native qubits
potential to coupling to flying qubits
- Various matterial systems, strong development driven by nanotechnology (CNT, graphene, nanowires)
Disadvantege:
Linear structure

## Slide 20
- Qubit:
½ spin of single electron trapped into
a confinement potential
R. Hanson, Rev Mod Phys, 79, 1217 (2007)
Spin Qubits
Notes: Advantages of spin qubits compare to other systems:
- Inherent scalability
Compatibility with existing microelectronics industry
well- defined native qubits
potential to coupling to flying qubits
- Various matterial systems, strong development driven by nanotechnology (CNT, graphene, nanowires)
Disadvantege:
Linear structure

## Slide 21
- Qubit:
½ spin of single electron trapped into
a confinement potential, Scalable system
Initialization of Qubits e.g. by B field
Single Qubit and by EDSR T≈150ns (2DEG) - 20ns (NW) Two-Qubit gates based on exchange int. T ≈ 200ps
Readout Pauli-spin blockade (fidelity>90%)
Fast decoherence T2 ≈ 10ns, T2* ≈ 1us Limited by hyperfine interaction
R. Hanson, Rev Mod Phys, 79, 1217 (2007)
Spin Qubits
Notes: Amazing degree of control on single electrons has been achieved during the last 5-10 years.
Advantages of spin qubits compare to other systems:
- Inherent scalability
Compatibility with existing microelectronics industry
well- defined native qubits
potential to coupling to flying qubits
- Various matterial systems, strong development driven by nanotechnology (CNT, graphene, nanowires)
Disadvantege:
Linear structure

## Slide 22
Spin Qubits, Various Material systems
- Nuclear spin free system: C, Si/Ge
Nuclear polarization
Faster operation: Singlet-Triplet Qubit
Topologic protection
…
Different materials
E.g. Si (28 purified)
E.g. Ge
W. I. L. Lawrie et al., Nat. Comm., 2023
T1~few s, T2~50 ms
M. Veldhorst et al., Nature Nano 2014
E.g. Graphene
Stampfer group, Aachen
Notes: Improve coherence… different material system. Fast development of nanotechnology is a great resource….
Various ways to improve, technological challanges
Nanowires where parts with long coherence time (Si) for memory, and strong SO interaction to operate
Topological protection: Majoran Fermions. Have zero spin and charge, well isolated from the outside world.
This reachness of systems gives the power of solid state quantum machines.

## Slide 23
1D architecture: interaction between neighboring qubits
Mobile entangled electrons
…
Images: Vandersypen lab, Delft
Notes: Coming back to the architecture. Qubits are in 1D array. Difficult to perform far distance operation. E.g. entanglment sending.
In addition quantum interfaces, convert info to other quantum system, e.g. for better isolation or better access.
Entanglement generation of flying spin qubits…

## Slide 24
Readout with microwaves
Fabry – Perot cavity for optics – using mirrors
Readout: Cavity QED
R.J. Schoelkopf et al., Nature 451, 664 (2009)
M. Göppl, : J. Appl. Phys. 104, 113904 (2008)
Using SC resonators to study artificial atoms
Large Q resonators
Notes: Coming back to the architecture. Qubits are in 1D array. Difficult to perform far distance operation. E.g. entanglment sending.
In addition quantum interfaces, convert info to other quantum system, e.g. for better isolation or better access.
Entanglement generation of flying spin qubits…

## Slide 25
Readout with microwaves
Readout: resonator frequency depends on qubit state
fr
X. Mi et al., Nature 2018
Coupling and readout of spin qubits using SC resonators
Spin to photon coupling of information
Notes: Coming back to the architecture. Qubits are in 1D array. Difficult to perform far distance operation. E.g. entanglment sending.
In addition quantum interfaces, convert info to other quantum system, e.g. for better isolation or better access.
Entanglement generation of flying spin qubits…

## Slide 26
Challenges
Needs low error rates <<1%
Maybe error correction
Better qubits?
Notes: Coming back to the architecture. Qubits are in 1D array. Difficult to perform far distance operation. E.g. entanglment sending.
In addition quantum interfaces, convert info to other quantum system, e.g. for better isolation or better access.
Entanglement generation of flying spin qubits…

## Slide 27
Scaling
Challenges:
Scaling up
72 qubits @ Google Bristlecone
European network for 100 qubit processor:
HUN Partners: BME & Wigner
Notes: Coming back to the architecture. Qubits are in 1D array. Difficult to perform far distance operation. E.g. entanglment sending.
In addition quantum interfaces, convert info to other quantum system, e.g. for better isolation or better access.
Entanglement generation of flying spin qubits…

## Slide 28
Research @ BME
Research direction: combine semiconductor/SC qubit properties
Develop novel qubit types that might be resistant to information loss (topological systems)
Notes: Coming back to the architecture. Qubits are in 1D array. Difficult to perform far distance operation. E.g. entanglment sending.
In addition quantum interfaces, convert info to other quantum system, e.g. for better isolation or better access.
Entanglement generation of flying spin qubits…

## Slide 29
Molecular
electronics
Spintronics
Lspin
Lφ
Le
LBohr
Quantumelectronics
Memristors
New Directions in Electronics
Notes: 29
To print: 1,4,5,7,8,9,15,16,18,23,24,25,26,29,30,31,34,35,40,41,43,46,47,48,51,55,60,61,62,63
Hosszutav jovo elektornikaja
Folztatni a miniaturiyalast  molekularis elektronika
Uj koncepciokat kidolgozni szamitasokra…
Kis meret tartomanyban maskeppen viselkedik egy eszkoz. Pl. Kvantummechanikailag,
Vagy ballisztikusan  elektron optika
Szamos objektum nanotechnologia teruleterol, amibol aramkoroket lehet kesziteni.

## Slide 30
K. Terabe et al., Adv. Mater 8, 536 (2007).
A possible realization of resistive switching
Positive bias (on the Ag electrode): Ag+ ions move towards the Me tip → an Ag filament is grown between the two electrodes → low resistance ON state
Ag2S memristor (memory + resistor): Ag electrode + thin Ag2S layer + electrochemically inert Me tip (e.g. PtIr or Nb).
I
V
RON
ROFF
Resistive Random Access Memory (ReRAM)
I(V) characteristics: linear resistive behavior at low bias, switching to ON/OFF state above a positive/negative threshold → ideal for memory operation
Negative bias: the Ag filament is destructed → high resistance OFF state

## Slide 31
Requirements against real ReRAM devices
Write/erase voltage level: < 2 Volt
Write/erase times: < 100 ns
Read-out voltage level: < 1 Volt
Read-out current level: ~ 0.001 – 1 mA
OFF to ON resistance ratio > 2
OFF state resistances < 100 kΩ
Endurance > 107 writing cycles
Retention times > 10 years
Non-volatility also during read-out operations
CMOS competitive scaling
CMOS compatible material systems and technology
A real resistive memory device must comply to ALL of the above requirements
R. Waser et al., Adv. Mat. 21, 2632 (2009).
J. J. Yang et al., Nat. Nanotech. 8, 13 (2013).

## Slide 32
ReRAM mass storage media
FLASH memory
FLASH
memory
performace
Crossbar ReRAM
Data created worldwide: >1018 byte/day
alltogether: >1022 byte
Further possibility: neuromorphic computing

## Slide 33
T. Hasegawa et al., Adv. Mat. 24, 252 (2012).
Close analogy to the human nervous system, including learning and forgetting abilities: ideal for neural network modeling
From nanoelectronics to neuroscience

## Slide 34
-Difficult to handle deep neural networks:
Key operation:
Vector-matrix multiplication
Software
implementation:
~n2 operations
Von Neumann computers
-Digital (0,1)
-Physically separated functionalities (processor & memory)
-General purpose hardware, software encoded tasks

## Slide 35
Neuromorphic computing
-Analog
-In memory computing
-Possible building blocks: memristors as artificial synapses
Memristive crossbar:
single-step
hardware multiplication

## Slide 36
How advanced is memristor technology?
Efficient and self-adaptive in-situ learning in multilayer memristor neural networks NATURE COMM. 9:2385 (2018)
128 x 64 Ta/HfO2/Pd crossbar
5-8 bit resolution
Training on MNIST handwritten digit database.
91.7% classification accuracy
1T1R arrangement, the transistor selects the devicies along the training, but oll transistors are open during inference
Notes: 11% unresponsive devices – self-adaption to hardware imperfecions
Simulations predict 97% accuracy with 1024x512 arrays

## Slide 37
How noisy are the memristors?

## Slide 38
What is the fastest switching?
10 picosecond switching (world record)

## Slide 39
Molecular
electronics
Spintronics
Lspin
Lφ
Le
LBohr
Quantumelectronics
Memristors
New Directions in Electronics
Notes: 39
To print: 1,4,5,7,8,9,15,16,18,23,24,25,26,29,30,31,34,35,40,41,43,46,47,48,51,55,60,61,62,63
Hosszutav jovo elektornikaja
Folztatni a miniaturiyalast  molekularis elektronika
Uj koncepciokat kidolgozni szamitasokra…
Kis meret tartomanyban maskeppen viselkedik egy eszkoz. Pl. Kvantummechanikailag,
Vagy ballisztikusan  elektron optika
Szamos objektum nanotechnologia teruleterol, amibol aramkoroket lehet kesziteni.

## Slide 40
Spin: internal degree of freedom
Stern-Gerlach experiment
4d105s1
Spin operator
  Spin in a magnetic field (Zeeman effect)
Magnetic moment
The torque acting on a spin in a homogeneous magnetic field
Hamiltonian

## Slide 41
  Ferromagnets
Origin exchange interaction (Coulomb interaction + Pauli principle)
Stoner model
Gain in Coulomb interaction if spin-polarized, but higher kinetic energy
In d-metals, with narrow band and high DOS spin-polarization can win
Magnetization
Spin polarization
Anisotropy (SO+crystal field or from shape)
Magnetization tends to align along certain directions
Magnetization dynamics
Slow rotation in perpendicular direction
Switching along the easy direction
Anisotropy protects magnetic state

## Slide 42
Nobel prize- 2007
GMR - Giant Magneto Resistance
P
RP<RAP
AP
GMR basic model:
Two separated current channels for spin up and spin down – no spin-flip scattering involved.
Description: resistor model - one spin species (P or AP with magnetization ) are scattered more due to different DOS. Result: increase of resistance for that channel (large resistor boxes).

## Slide 43
Nobel prize- 2007
P
RP<RAP
AP
GMR basic model:
Two separated current channels for spin up and spin down – no spin-flip scattering involved.
Description: resistor model - one spin species (P or AP with magnetization ) are scattered more due to different DOS. Result: increase of resistance for that channel (large resistor boxes).
The magnetization of one of the layers can be fixed (e.g. with an antiferromagnet – single switching
GMR - Giant Magneto Resistance

## Slide 44
Tunnel barrier between two magnetic layers
Growth of oxides with atomic precision
TMR - Tunneling Magneto Resistance
The current is proportional to the DOS (both initial and final state). The current will be different in the P and AP configuration. Spin conserving tunneling assumed.
Giant spin signals can be achieved
The structure is often called spin-valve
Polarizáció

## Slide 45
Magnetic data storage
GMR/TMR sensors are used also in the read head of hard drives. Hard drives contain small magnetic islands.
Readout: the magnetic field of the island will flip the sensor.
Writing: inductive coupling – writing currents
TMR spin valves are also used in memory cells:
MRAM - 0 and 1-s are encoded to single spin valves
Readout : small current via TMR effect
Writing: passing current on the bit and word lines at the same time
Magnetic domains in an HDD imaged by TEM
Source: T. Santos

## Slide 46
FM-NM interface
Full description: Valet-Fert model relying on the Boltzmann equation applied for two subbands.
current
diffusive spin transport:
The non-equilibrium imbalance in the subband occupation results in a difference in the chemical potential corresponding to the different spin-subbands. This difference decays toward the bulk of the non-magnetic metal
J. Bass et al., J. Phys.: Condens. Matter 19, 183201 (2007)
G. Schmidt et al., PRB 62, R4790 (2000)
The spin polarization drops at the interface
very low efficiency for semiconductors
OK for metals and graphene
exponential cutoff:
the amplitude of the GMR is proportional to the remaining spin polarization
Spin injection

## Slide 47
N. Tombros et al, Nature, 448, 571 (2007)
The imbalance of the chemical potentials can be detected, without the interference of the direct current path
As the in-plane field is swept both the detector and injector switches (at different fields)
From several samples, spin-diffusion length obtained
Non-local spin measurement

## Slide 48
Hanle spin precession measurement
In a 1D ballistic system a cosine precession is expected
Diffusion and relaxation makes it more complex
Spin relaxation time can be obtained from fitting
P/AP the sign is opposite
rotation of 180°
Larmor frequency
N. Tombros et al, Nature, 448, 571 (2007)

## Slide 49
Quasi-classical description: the charge carriers moving in a perpendicular magnetic field are deflected due to the Lorentz force
An electric field along the y coordinate is built up in the sample
y
No net voltage drops along the y direction, but an opposite spin polarization arises at the edges
y
Small effect (106A/cm2):
J. E. Hirsch, Phys. Rev. Lett. 83, 1834 (1999)
Does not require an external magnetic field nor a FM electrode!
Spin Hall effect
ki
kf
Y. K. Kato et al., Science 306, 1910 (2004).
Spin polarization – detected by magneto optics
Hall effect:

## Slide 50
How to measure it?
Idea: if the incident current is already spin polarized, then a measureable voltage develops (e.g. more down spins accumulate than up spins  Hall voltage)
Spin injection: using FM contacts
In actual nonlocal experiments, there is no net current through the device, but spin diffusion/current appears
magnetic field
At zero B-field magnet polarization is in-plane.
j ~ js  s, out-of-plane magnetic field (and spinpol) is necessary to have a transverse spin current and a Hall voltage
the device is characterized using FM2 in a standard nonlocal measurement
S. O. Valenzuela and M. Tinkham, Nature, 442, 176 (2006)
  Inverse spin Hall effect

## Slide 51
previously: versatile devices, but an external magnetic field is necessary to manipulate spin states. All electric control would be better.
free layer
I
spin polarized current
I
spin polarized current
The free layer is rotated by the current instead of the external magnetic field. The structures are however similar.
Potential application: memory cell
write: STT with high current pulse
read: GMR/TMR at low current
Current density: 109 A/cm2
Only feasible at the nanometer-scale!
Dominate above Oersted fields
Heating happens away from the contact region
D. C. Ralph et al., J. of Magn. Mag. Mater. 320, 1190 (2007)
  Spin transfer torque

## Slide 52
  Spin orbit torque
Spin orbit torque:
Spin polarization is generated in the substrate with large SOC using a current. The mechanism is either SHE effect or Rashba Edelstein effect.
The SOC generated spin current switches the FM.
Readout: e.g. via anomalous Hall effect
Spin orbit switching
Co with out of plane magnetization (extra thin) Pt Hall cross. With current generate spin polarization which acts with a torque on the FM.
Readout: measure Hall voltage on the heterostructure – AHE in the FM material
I. M. Miron et al., Nature, 476, 189 (2011)

## Slide 53
  Spintronics
Literature:
J. Fabian et al., Semiconductor spintronics, Acta Physica Slovaca 57, 565 (2007) and arXiv:0711.1461
I. Zutic, J. Fabian and S. Das Sarma, Spintronics: Fundamentals and applications, Rev. Mod. Phys. 76, 323 (2004)
D. C. Ralph and M. D. Stiles, Spin transfer torques, J. Magn. Mag. Mater. 320, 1190 (2007)
T. Jungwirth et al., Spin Hall effect devices, Nat. Materials 11, 382 (2012)
and more.... See references
Nanofizika tudásbázis, fizipedia.bme.hu (in Hungarian)